## Slide 1
COLOR SPACES
OTHER THAN
RGB CMY HSV
COMPUTER VISION
AD-23402
SYED HARSHATH S
2023510045

## Slide 2: INTRODUCTION
Many colour spaces exist beyond RGB, CMY, and HSV
Designed for specific applications like compression, printing, perceptual modelling

## Slide 3: Why Do We Need Other Color Spaces?
Different tasks need different color representations
Separate brightness and color for compression
Perceptually uniform spaces for editing and printing

## Slide 4
YPbPr (also written Y'PbPr) is a color space used in analog video electronics.
Similar to YCbCr but designed for analog signals, while YCbCr is for digital video.
Commonly referred to as component video in consumer electronics.
YPbPr

## Slide 5: RELATION TO RGB
Derived from gamma-corrected RGB (R'G'B') signals.
Separates image into:
  Y' (Luma / brightness)
  Pb (Blue difference chroma)
  Pr (Red difference chroma)

## Slide 6: Mathematical Definitions
Luma (Y') equations:
HDTV: Y' = 0.2126R + 0.7152G + 0.0722B
SDTV: Y' = 0.299R + 0.587G + 0.114B
Chrominance:
Pb = 0.564(B' - Y') (SDTV)
Pr = 0.713(R' - Y') (SDTV)

## Slide 8: Signal Characteristics
Carries sync information on Y' channel (bi-level for SD, tri-level for HD).
Signals range from 0 to 700 mV (analog voltage levels).
Does not need color multiplexing → minimal color bleeding.

## Slide 9: ADVANTAGES
Better image quality than composite or S-Video.
Supports higher resolutions: up to 1080p (Full HD).
Compatible with standard RCA cables (green = Y, blue = Pb, red = Pr).
Used in:
  DVD players
  Set-top boxes
  Video game consoles
  Older HDTVs
PRACTICAL USAGE

## Slide 10: HSL
HSL (Hue, Saturation, Lightness) is a cylindrical-coordinate representations of RGB colors.
They rearrange RGB space to be more intuitive and perceptually relevant for humans.
Commonly used in color pickers, image editing software, and (to a lesser extent) computer vision.

## Slide 11: Structure
Both models are based on a cylinder:
  Hue (H): angle around the vertical axis (0° = red, 120° = green, 240° = blue, 360° wraps back to red).
  Saturation (S): distance from the center axis (color purity).
  Lightness (L) / Value (V): position along the vertical axis (brightness or luminance).

## Slide 12: Relation to RGB
HSL and HSV are just transformations of the RGB color model.
The specific output color depends on the RGB space (e.g., sRGB, Adobe RGB) and device-specific properties like gamma correction.

## Slide 13: RGB → HSL conversion formulas
Compute min, max, delta:
Cmax = max(R, G, B)
Cmin = min(R, G, B)
delta = Cmax – Cmin
Lightness (L):
L = (Cmax + Cmin) / 2

## Slide 14
Saturation (S):
if delta == 0: S = 0 else: S = delta / (1 - abs(2*L - 1))
Hue (H):
if delta == 0: H = 0
elif Cmax == R: H = 60 * (((G - B) / delta) % 6)
elif Cmax == G: H = 60 * (((B - R) / delta) + 2)
elif Cmax == B: H = 60 * (((R - G) / delta) + 4)

## Slide 15
RGB TO HSL

## Slide 16
HUE SATURATION LIGHTNESS

## Slide 17: Motivation
RGB is device-centric and unintuitive for tasks like adjusting brightness or mixing tints/shades.
HSL/HSV provide models closer to traditional art concepts (e.g., tints, shades, tones).
Their simple math made them practical for 1970s computers.

## Slide 18
LIMITATIONS
Not perceptually uniform: small changes in HSL/HSV don’t correspond to equally perceived color differences.
Models like CIELAB or CIECAM02 are better at representing perceptual differences but are more computationally complex.

## Slide 19
Aspect | HSV (Hue, Saturation, Value) | HSL (Hue, Saturation, Lightness)
Brightness axis | Measures brightness (value) from black (0) to full color (1) | Measures lightness from black (0), through pure color (0.5), to white (1)
Full saturation level | Full saturation colors are always at V=1 (top of cone) | Full saturation colors are at L=0.5 (middle of bicone)
Saturation meaning | Measures how much black is mixed with the color | Measures how much gray is mixed with the color
Model shape | Hexcone (cone) | Bi-hexcone (double cone or diamond shape)
White mixing behavior | Adding white reduces value but keeps saturation constant | Adding white reduces saturation

## Slide 20: YIQ Color Space
YIQ is the color space used by the NTSC analog TV system
(mainly in North America and Japan).
It separates an image into:
Y (Luma): brightness (black-and-white image)
I (In-phase): orange-blue chrominance
Q (Quadrature): purple-green chrominance
Black-and-white TVs only decode Y → backward compatibility.

## Slide 21: Why YIQ?
Human eyes are more sensitive to orange-blue (I) than purple-green (Q). Therefore: I gets higher bandwidth (1.3 MHz) Q gets lower bandwidth (0.4 MHz) Designed to optimize bandwidth while preserving perceptual quality.

## Slide 22: YIQ vs Other Color Spaces
COLOR SYSTEM | COLOR SPACE
NTSC | YIQ
PAL | YUV
SECAM | YDbDr
Digital TV | YCbCr

## Slide 23: Conversion Equations
RGB to YIQ:
YIQ to RGB:

## Slide 24
YIQ COLOR MODEL

## Slide 25: YIQ ↔️ YUV Relationship
YIQ is a rotation of YUV by 33° in UV plane:
Both share same luma axis; differ in chrominance axis.

## Slide 26: Practical Usage
Rarely implemented in modern TVs → simpler R-Y / B-Y decoders were cheaper.
Some high-end TVs (e.g., RCA Colortrak, Advent) used full I/Q decoding for better color fidelity.

## Slide 27: CONCLUSION
In this presentation, we explored different color spaces such as YPbPr, HSL, and YIQ, understanding their structures, mathematical conversions, and real-world applications.
YPbPr represents color with luminance and chrominance components, they are used in analog and digital systems respectively.
Color spaces like HSL and YIQ offer intuitive or broadcast-friendly ways to represent colors for specific tasks.